## Slide 1: Reliable Multicast For RTM

## Slide 2: Outline
New Transport Protocol for RTM
  Motivation and Design goals
Multicast Performance
  One-to-one connection Case
  Fan-out model Case
  Fan-in model Case
Reliable UDP Multicast (RM-UDP) Solution
  Current NSQ Design
  Design Assumptions and Considerations
Design of RM-UDP
  NSQd address management and lookup
  NSQd and Consumer communication

## Slide 3: New Transport Protocol for RTM
Motivation
  Large number of concurrent connections between NSQ Daemon and Subscribers causes CPU contention and then leads to high latency for message delivery.
  Need a new transport protocol for connections between NSQ Daemon and Subscribers to alleviate CPU contention.
Design Goals
  Low Latency: achieve low latency for message delivery
  Scalability: allow RTM to scale to large number of subscribers
  Reliability: guarantee reliable message delivery
Previous investigation: UDP and TCP
  UDP has slightly lower latency and lower CPU utilization than TCP
  However, for both protocols, CPU utilization and latency dramatically increase as the number of subscribers increases.
Another direction to explore
  Multicast, as it leverages the network for one-to-many message delivery
  What’s the performance of multicast?

## Slide 4: Outline
New Transport Protocol for RTM
  Motivation and Design goals
Multicast Performance
  One-to-one connection Case
  Fan-out model Case
  Fan-in model Case
Reliable UDP Multicast (RM-UDP) Solution
  Current NSQ design
  Design Assumptions and Considerations
Design of RM-UDP
  NSQd address management and lookup
  NSQd and Consumer communication

## Slide 5: Multicast Performance
Multicast Performance Test Environment
  Programs written in golang (as NSQ) using x/net/ipv4 package for multicast socket
  Tested on Two Huawei machines connected through a switch.
One-to-one connection Case Setup
  On one server, a simple sender keeps sending packets to a multicast address
  On the other server, a receiver program receives packets from the address
One-to-one connection Case Results
  Throughput of multicast is worse than that of TCP or UDP
    TCP is max at 7.4 Gbps
    UDP is around 2.7 Gbps
    Multicast is 1.2 Gbps
  Latency of multicast falls between TCP and UDP
    TCP is around 0.1 ms
    UDP is around 0.05 ms
    Multicast is around 0.07 ms

## Slide 6: Multicast Performance
Fan-out Model Case Setup (one-to-many)
  Sender and receiver run on two different machines (Huawei S1 and S2).
  One message generation goroutine at sender side, multiple receive goroutines at receiver side
    Message generation goroutine generates signal sending to sending goroutine(s) every 5ms which triggers the sending goroutine sending a 1000bytes message.
    For TCP/UDP: one sending goroutine at sender side corresponds to each receiving goroutine at receiver side with TCP/UDP connection
    For Multicast: only one sending goroutine at sender side, it sends to message through multicast socket, each receiving goroutine reads from same multicast address.

## Slide 7: Multicast Performance
Fan-out Model Case Results
  Latency: for different level of concurrency (in terms of number of receiving goroutines), multicast has lower latency than TCP and slightly higher latency than UDP. There’s no significant latency benefit of multicast for fan-out. This is likely because the receiver side is a bottleneck limiting multicast performance.
  CPU utilization: on the sender side, multicast has much lower CPU utilization than TCP and UDP, since multicast messages are sent through only one socket.
Chart: Protocol and Number of Concurrent Connections
| TCP 64 | UDP 64 | MTC 64 | TCP 128 | UDP 128 | MTC 128 | TCP 256 | UDP 256 | MTC 256 | TCP 512 | UDP 512 | MTC 512
usr cpu | 6.5 | 6.5 | 0.9 | 12 | 11.7 | 0.9 | 21.4 | 21.5 | 1 | 30 | 36.3 | 0.9
sys cpu | 21 | 19 | 2.2 | 40 | 34.4 | 2.3 | 70.3 | 65 | 2.1 | 106.4 | 109 | 2.3

## Slide 8: Multicast Performance
Revised Fan-out Model Case Setup
  Remove receiver side bottleneck
  Use three machines instead of two
    One server (huawei1) as sender, and two other machines as receivers
    One receiver (on huawei2) runs multiple receiver goroutines whereas the other receiver (on huawei3) runs only one goroutine.
  Measure only the latency of a single goroutine (on huawei3), whereas in previous model, we sampled latency from all goroutines and averaged them.
  For TCP/UDP, sending goroutines send out message in an order, the order also affects the latency for each connection.

## Slide 9: Multicast Performance
Revised Fan-out Model Case Results
  Two comparisons: the unicast connection to the goroutine receiver is 1) the first one to send message, 2) the last one to send message.
  Latency: For both cases, the latency of multicast is smaller than TCP and UDP. For the first case, the latency of TCP and UDP remain at the same level as we increase concurrency. However, for the second case, they increase dramatically as concurrency increases. Multicast reduces the latency by removing message copy and sending in sender.
First one to send message
Last one to send message

## Slide 10: Multicast Performance
Fan-in Model Case Setup (many-to-one)
  Sender and receiver run on two different machines (Huawei S1 and S2).
  Multiple message generation goroutines and one sending goroutine on sender side, and one receiving goroutine on receiver side.
    Each message generation goroutine generates signal to sending goroutine every 5ms which triggers the sending goroutine sending a 1000bytes message.
    Only one socket connection between sender and receiver, which is handled by the sending goroutine at the sender side and receiving goroutine at the receiver side.

## Slide 11: Multicast Performance
Fan-in Model Case Results
  Latency: for different level of concurrency (in terms of number of message generation goroutines), multicast has slightly higher latency than UDP, and lower latency than TCP.
  CPU utilization: for all cases, CPU utilization of multicast is higher than TCP, for most cases (except for 512), multicast has higher CPU utilization than UDP, though not by a lot.
Chart: Protocol and Number of Concurrent Connections
| TCP 64 | UDP 64 | MTC 64 | TCP 128 | UDP 128 | MTC 128 | TCP 256 | UDP 256 | MTC 256 | TCP 512 | UDP 512 | MTC 512
usr cpu | 14 | 14 | 16 | 25 | 25 | 30 | 40 | 43 | 45.5 | 62 | 65 | 48
sys cpu | 22 | 23 | 29 | 39 | 38 | 51 | 52 | 59 | 73 | 61 | 73 | 81

## Slide 12: Multicast Performance
Conclusion About Multicast Performance
  For fan-in model (i.e., many-to-one or one-to-one), UDP multicast has slightly higher latency than UDP but lower latency than TCP. Multicast has typically slightly higher CPU utilization than TCP and UDP.
    This is not a primary candidate for multicast, i.e., only one connection, but even in that scenario multicast does not do much worse, latency-wise, than unicast
  For fan-out model (i.e., one-to-many which is common in pub-sub system), the overall CPU utilization for multicast is dramatically lower, since it only needs to send each message once. The latency of multicast is lower than TCP and UDP.
    This is the primary scenario where multicast is beneficial
    Multicast offloads copy and sending to multiple destinations from sender to network.
Drawbacks of Multicast
  It requires network support of multicast. Need to have control over that network capability to ensure support for RTM multicast solution
  The transmission (network) paths of multicast packets can be different from unicast. That means different propagation delay and forwarding delays (this is not present in our experiments, since sender and receiver are only one-hop away from each other).

## Slide 13: Outline
New Transport Protocol for RTM
  Motivation and Design goals
Multicast Performance
  One-to-one connection Case
  Fan-out model Case
  Fan-in model Case
Reliable UDP Multicast (RM-UDP) Solution
  Current NSQ Design
  Design Assumptions and Considerations
Design of RM-UDP
  NSQd address management and lookup
  NSQd and Consumer communication

## Slide 14: Current NSQ Design
NSQd Address Management and Lookup
  1. NSQd connects to NDQLookupd and register/unregister topic/channel
  2. NSQLookupd creates databases to store daemon, topic, and channel info
  3. Consumer queries NSQd information for certain topic
  4. NSQLookupd returns the information of NSQds registered for the topic

## Slide 15: Current NSQ Design
Consumer and NSQd Communication
  5. Consumer connects to each NSQd returned from NSQLookupd
  6. NSQd generates client and IOLoop, Messagepump goroutines for each connection
  7. Consumer sends SUB message to subscribe topic and channel.
  8, 9. NSQd sends published messages to each consumer, consumer acknowledges each message with FIN message. RDY message for sending rate control between daemon and consumer, and HEARTBEAT message for liveness check.

## Slide 16: Reliable UDP Multicast – Design Assumptions
Assumption 1: in-order delivery for the network in most cases
  Most network devices deliver packets of a given flow in order. We, therefore, assume that end-to-end in-order delivery is the norm, and violated only in rare cases, like path changes.
  This assumption helps simplify packet processing and reduce the time for detecting message loss, i.e., receipt of an out-of-order message means a packet loss.
  Violation of this assumption only leads to redundant messages (false positive detection of message loss), and does not affect operational correctness.
Assumption 2: message loss is relatively rare.
  The system is deployed in a well provisioned network, where message losses are be relatively rare, i.e., congestion is not common
  Under this assumption, a linear list offers a simple yet efficient way to store message loss information.
  Violation of this assumption leads to (linear) increase in search time for lost packets, but does not affect correctness.

## Slide 17: Reliable UDP Multicast – Design Assumptions
Assumption 3: messages are independent of each other and timeliness of delivery is important, i.e., stale messages are not useful
  A message is no longer wanted if it is not received after a certain time (consistent with our goal of low latency). Messages are atomic, i.e., a message content does not depend on other messages.
  This enables a simple and scalable reliability mechanism that delivers messages in the order in which they are actually received. (An in-order delivery can be enforced with reordering in application level)
  A consequence of this assumption is that some list messages may never be recovered (once a certain retransmission time period is exceeded). Consumers that require 100% reliability should use unicast instead of multicast.

## Slide 18: Reliable UDP Multicast Solution
Design Considerations For Multicast
  Multicast address management
    One multicast address per topic
      For a given topic, the same multicast address is used across all daemons with producers publishing to the topic.
      This reduces the number of connections on the consumer side, and the number of multicast addresses used.
    A mechanism is needed to manage assignment of multicast addresses to topics. The NSQlookup daemon is a natural candidate for performing such function.
      The NSQlookup daemon will return the multicast address assigned to a topic, when an NSQd registers for the topic.
  Reliable Transmission
    Acknowledgement of each message for reliability requires tracking the ACK state of individual consumers which is not scalable when the number of consumers is large (ACK volume can overwhelm NSQd).
    Therefore, NACK is used instead, a NACK indicate message loss detected.
      NSQd only reacts to NACKs without tracking the state of individual consumers.
    A message must remain in NSQd in-flight queue until all consumers can be assumed to have received it (no NACK for the message received after certain time)

## Slide 19: Reliable UDP Multicast Solution
Additional Considerations
  Tracking consumer info
    Tracking consumer info would require separate exchanges (when joining and leaving). This could be expensive when the number of consumers is large, but is a one time operation.
    Because joining a multicast group does not require interacting with NSQd, we lose the ability to track which customers subscribe to a given topic
      This capability can be added back through an out-of-band hand-shake
  Congestion control between NSQd and consumer
    RTM already includes topic-level rate control between producers and NSQd
    Additional rate control may possibly be realized by adjusting in-flight queue based on NACK information (more NACK means congestion at least for some consumers), but using that information can be problematic (how to set “correct” transmission rate across heterogeneous receivers?)
  Tradeoff between Reliability, Latency, and Resources
    Greater reliability can be realized by increasing the safe-time (the time a message stays in in-flight queue). This will, however, require a larger in-flight queue size or result in longer latency due to blocking of message transmissions because of full in-flight queue.
    Faster retransmissions in cases of multiple losses call for more aggressive reporting of lost messages by consumers. This would likely result in more retransmissions and consequently message duplication and greater resources consumption.
  Heterogeneous consumers
    Individual consumers may require stronger reliability than multicast can offer
    Such consumers may be allowed to use TCP unicast instead, if there are few of them

## Slide 20: Outline
New Transport Protocol for RTM
  Motivation and Design goals
Multicast Performance
  One-to-one connection Case
  Fan-out model Case
  Fan-in model Case
Reliable UDP Multicast (RM-UDP) Solution
  Current NSQ Design
  Design Assumptions and Considerations
Design of RM-UDP
  NSQd address management and lookup
  NSQd and Consumer communication

## Slide 21: Design of RM-UDP
NSQLookupd address management
  When multicast is enabled in NSQLookupd (with multicast_flag), it reserves some multicast addresses in the network and UDP ports on each server. It also maintains available multicast addresses and ports and used ones.
  When NSQd registers itself to a topic, NSQLookupd returns the multicast address and port corresponding for the topic. If the topic is new, then NSQLookupd assigns a new multicast address and port to the topic, and returns the assigned address and port.
NSQd lookup in Consumer
  Consumer queries NSQLookupd for NSQd info on a given topic
  It returns NSQd information related to that topic.
    NSQLookupd returns the information (unicast address) of NSQds that publish the topic and the multicast address/port for the topic.
    Consumer can uses multicast address if it wants to subscribe to multicast channel of the topic. Otherwise, it connects to all NSQds using unicast address for other channels.

## Slide 22: Design of RM-UDP
Consumer and NSQd Communication
  Connection Setup
    After NSQd registers a topic and receives the multicast address for the topic, it creates a client and a channel specific for multicast (named “multicast”) using the assigned multicast address (see slide 14 for the detailed structure of a client and channel)
    Consumer who subscribes to multicast channel of topic simply joins (local multicast functionality) and listening to the multicast address of the topic (no explicit sending of SUB message)
    HEARTBEAT messages are sent every heartbeat interval.
    RDY messages and FIN messages sent from consumers are disabled.
  Connection Cleanup
    When NSQd wants to close multicast connection, it can either actively sends a CLOSE message to multicast connection before it closes the connection, or it simply closes the connection.
    Consumer closes multicast connection when it receives a CLOSE message or no message (including HEARTBEAT message) are received for several heartbeat intervals.

## Slide 23: Design of RM-UDP
Consumer and NSQd Communication
  Message Sending (Daemon)
    NSQd sends/resends message to the multicast address when signaled to, it also maintains each message along with its message id, first send timestamp and last send timestamp using in-flight queue.
    If no message sent out for last-send-timeout, NSQd sends up to max-null-send NULL messages to ensure the receiver can detect message loss for last sent message in a timely fashion. (see slide 28 for more details about NULL message)
    A message in in-flight queue times out if
      more than max_hard_timeout has elapsed since it was first sent,
      or more than message_safe_timeout has elapsed since it was last sent.
    Timed-out message is removed from in-flight queue. (see slide 29 for details about checking message timeout)

## Slide 24: Design of RM-UDP
Consumer and NSQd Communication
  Lost Message Retransmission (Daemon)
    When NSQd receives a NACK for a message, it first checks if the message is still in in-flight_queue. If it’s, do following.
    If previous NACK (for the same message id) does not exist, resend the message (through multicast), add the sender (of the NACK) to resend_msg_list.
    If previous NACK exists
      and is sent from the same sender, resend the message (through multicast), empty resend_msg_list for the message, add only the sender.
      and is not sent from the sender, append the sender to resend_msg_list for the message.
    The message sending process will remove a message from resend_msg_list when the message is removed from in_flight_queue.

## Slide 25: Design of RM-UDP
Consumer and NSQd Communication
  Message Loss Detection (Consumer)
    When receiving a regular message from a daemon, we update the last_send_id for that daemon.
    A message loss is detected when
      Arrived message with message id larger than last_send_id +1
      Arrived NULL message with larger message id than last_send_id
    After a loss is detected, NACK message is sent to corresponding NSQd with message id of lost message(s), and related information (message id, timestamps of first NACK send time and last NACK send time) is stored in lost_msg_list.
    A NACK will be only be resent when nack_resend_timeout has elapsed after NACK of the message was last sent, and retransmission has not been received
    Message will be removed from lost_msg_list if the retransmission of message is received or max_hard_timeout has elapsed since the NACK of the message was first sent. (see slide 29 for detail about checking message timeout)

## Slide 26: Design of RM-UDP
Consumer and NSQd Communication
  Parameters
    message_safe_timeout: represents the maximal period of time for daemon to be aware of message loss and resend a message.
      should be set to slightly larger than max_rtt + max_null_send * last_send_timeout + 2n* nack_resend_timeout, to allow recovery of at least max_null_send consecutive lost messages and n NACK/message retransmission losses. n could be set to 1. (see slides 28 and 29 for details about the reasoning),
    max_rtt: allowed maximal round trip time between NSQd and consumer for basic multicast reliability, any consumer with a larger RTT will have a lower level of reliability. A larger max_rtt means more tolerance for consumers with large RTT.
    max_null_send: represents the maximum number of null messages to send after a regular message (see slides 28 for details about NULL message). Larger value means multicast can handle more complicated cases for message loss.
      can be set to 2 or 3.
    last_send_timeout: represents the interval to send a NULL message after a regular or NULL message (see slides 28 for details about NULL message). Smaller last_send_timeout means lower latency for detecting message loss, but also leads to more NULL messages.
      can be set to larger than the average message interval.

## Slide 27: Design of RM-UDP
Consumer and NSQd Communication
  Parameters
    nack_resend_timeout: represents the time for consumer to resent NACK if lost message has not been received by consumer.
      can be set by each consumer to slightly larger than its RTT to daemon. If the RTT is not known, it can be set to slightly larger than max_rtt.
    max_hard_timeout: represents the maximum period of time available for daemon/consumer to achieve message reliability.
      If message loss has not been resolved after this period since message first sent, then daemon will stop resending the message, and remove it from in_flight_queue
      If message loss has not been resolved after this period since message loss first detected, then consumer will stop resending NACK messages and remove it from loss_msg_list.
  Tradeoff among those parameters
    For better Latency for recovery from loss:
      Smaller last_send_timeout, nack_resend_timeout
    For better Reliability:
      Larger max_rtt, larger max_null_send , larger max_hard_timeout, and larger n
    For less Memory:
      Smaller message_safe_timeout, and smaller max_hard_timeout
    For less Traffic:
      Larger last_send_timeout

## Slide 28: Design of RM-UDP
Other Design Details
  NULL message for timely message loss detection
    It could be that a message is sent and for a long time no message is sent. Then it would be too late for the receiver to detect the loss of the last message.
    We send NULL message containing the message id of last send message by the daemon if no message is sent for null_send_timeout. And we will send up to max_null_sent, in case NULL message is also lost.
    So that receiver (consumer) will detect the loss within max_null_sent *null_send_timeout which allowing at most max_null_sent -1 NULL message losses.
    Unlike heartbeat, NULL message will stop after continuously sending max_null_sent NULL messages to avoid unnecessary traffic.
  Use timestamp instead of Timers for timeout
    For message sending timeout and NACK message sending timeout, we use timestamps to track the sending/resending time of messages and check the timeout of message based on those timestamps, avoiding using individual timer which saves computing resources.
    Also, priority queue is used, based on timeout of each message, finding timeout message(s) is quick.
    The side effect of using timestamp is delaying the time for detecting timeout.

## Slide 29: Design of RM-UDP
Other Design Details
  Check timeout using timestamp
    For message sending, timeout is checked whenever something message needs to be sent or resent. This delays message timeout for uncertain amount of time. However, this only delays the removal of message from in_flight_queue, does not affecting correctness. And message timeout will be checked after sending a message, therefore, it has nearly no effects on in-flight queue size.
    For message loss detection, timeout is checked when we receive a message or there’s not checking for nack_resend_timeout. It delays message timeout for at most nack_resend_timeout. Therefore, at most 2* nack_resend_timeout is needed to resend a NACK.
  Limiting size of in_flight_queue
    When we have large message_safe_timeout and large max_hard_timeout, the size of in_flight_queue can be large when message rate is high.
    A potential solution is limiting the size of in_flight_queue, when the size of in_flight_queue reaches the limit, after each message added, we remove the oldest message (even though it has not yet timed-out)
      This weakens reliability when the message rate is high.

## Slide 30: Distributed NSQLookupd
Multiple NSQLookupds
  The multicast address of a topic should be global unique
  NSQLookupds should return the same multicast address for a topic
Proposal: address management designated nsqlookupd
  Elect one designated NSQlookupd for multicast address management, for other NSQlookupds, the management function is deactivated.
  For a new topic, first check local database for multicast address, if not exist, get address from multicast address management in designated NSQlookupd.
  The multicast address database (map of address and topic) are synchronized among NSQlookupds when it is changed in designated NSQlookupd.