## Slide 1: RTM A New Real-Time Messaging Middleware -- A Transport Protocol For RTM
Washington University
Project Report
Oct. 20, 2016

## Slide 2: Outline
Connections in RTM
Design Goal
Existing Protocols or Solutions
TCP vs. UDP Performance
  Experiment Setup
  One-to-one Connection
  Fan-out Model
  Fan-in Model
Proposal
  Approach: Reliable Multicast UDP

## Slide 3: Connections in RTM
Connections with Lookup Daemon
  Publisher and Lookup Daemon
    One-time connection, exchange setup information
  Subscriber and Lookup Daemon
    One-time connection, exchange setup information
  RTM Daemon and Lookup Daemon
    Persistent connection, setup and update configuration information
Connection characteristics
  Low concurrency, either one-time connection or limited number of persistent connections (only 10s of RTM daemons)
  Low traffic, not much information is exchanged.
TCP is a good enough since it’s already highly optimized and provides reliability and retransmission.

## Slide 4: Connections in RTM (cont.)
Connections with RTM Daemon
  Publishers and RTM Daemon
    Persistent connection, 100s of publishers send messages to Daemon and Daemon sends back message acks
  RTM Daemon and Subscribers
    Persistent connection, daemon sends messages to subscribers (up to 1000s), and subscribers send back message acks
Connection characteristics
  High concurrency, one-to-many message transmission or many-to-one message transmission
  Experiments identified scenarios with potential for high latency for connections between RTM Daemon and subscribers
    Main scalability problem: 1000s of subscribers
Transport protocol should be scalable and able to handle high transmission concurrency

## Slide 5: Design Goal
Transport protocol For RTM
  Performance
    Minimize per message latency between daemon and subscriber
    Preserve high message throughput
    Minimize CPU consumption
  Scalability
    Ability to scale to 1000s concurrent connections
  Reliability
    Reliable delivery of messages (either through transport or application level reliability)
    In-order message delivery optional, since in-order hurts latency when message loss happens.

## Slide 6: Existing Protocols or Solutions
TCP
  Widely used and highly optimized in current network stack
  Already provides reliability and high throughput
  But does not guarantee latency
Variations or improvements based on TCP
  Reduce blocking latency with smart framing [1]
  Low-latency Adaptive Streaming [2]
UDP
  Datagram, light weight transport protocol
UDP based Reliable Transport Protocol
  UDT: reliable data transfer for high-speed wide area network [3]
  Aeron: reliable and low latency UDP messaging system [4]
Efficient network stack for multicore environment
  mTCP: user-space stack [5]
  Megapipe: scalable network I/O [6]
  Fastsocket: highly scalable socket for multicore [7]

## Slide 7: Existing Protocols or Solutions (cont.)
Comments on Current Solutions
  Most works focus on improving throughput rather than reducing latency, and may therefore be unsuitable for the latter (e.g., batching hurts latency).
  Most UDP and TCP extensions (except for multicore extensions) are ~10 years old, and ignore many TCP stack and NIC optimizations undertaken over the years.
  None of the UDP and TCP extensions aims to address scalability or high concurrency.
We first need to
  Benchmark the performance of TCP and UDP in the current Linux Kernel.
  Evaluate differences introduced by go language, since our RTM is based on NSQ which is written in go.
  Emulate the RTM scenarios for Fan-in and Fan-out, and then do a comparative evaluation of the latency with TCP and UDP (which indicates the relative performance of TCP and UDP)

## Slide 8: TCP vs. UDP Performance
Benchmark TCP and UDP performance for one-to-one connection
  Linux kernel raw performance
    For this part, we intend to measure and explore the performance and limitation of TCP and UDP in Linux kernel
    Write C program that directly calls sys calls to measure the performance of Linux kernel for TCP and UDP
  Go language interface performance
    Go language wraps socket related sys calls, and it also uses goroutines for scheduling. All may affect the performance. We intend to evaluate the performance and compare it with Linux kernel performance.
    Write program with Go language calling Go net interface
Benchmark the relative performance of TCP and UDP in RTM scenarios
  Write programs with Go language to emulate two RTM scenarios for Daemon and subscriber connection.
  Fan-in model: Messages from multiple sources are aggregated and sent through one connection
  Fan-out model: Messages from single source are sent to multiple connections
Notes: Emulating with golang for simulation

## Slide 9: Experimental Setup
Configurations
  Two servers from Huawei, (s1 and s2)
    CPU Intel(R) Xeon(R) CPU E5-2660 with 40 cores, 126 GB memory
    OS: CentOS Linux release 7.2.1511, kernel version: 3.10.0-327.28.3.el7.x86_64
    Only 2 cores are used in Fan-in and Fan-out scenarios, to create CPU contention with relatively small number of connections (RTM Daemon runs in a CPU contention environment).
Tuning for TCP and UDP
  TCP socket with TCP_NODELAY option to disable Nagle’s algorithm, send small packets immediately to minimize latency
  UDP send/receive buffer set to 4MB to avoid losses
See document “Tuning document” for additional parameter tunings for performance in 10G/100G.

## Slide 10: One-to-One Connection
Chart: Implementation Language and Protocol
| GO TCP | GO UDP | C TCP | c udp
Throughput | 6.9 | 2.8 | 9.8 | 5.99
Benchmark TCP and UDP performance
  Sender (with single thread/go routine) keeps sending 1000 bytes packets in a for loop without wait or sleep.
  Result:
    Go language net interface introduces overheads (due to extra function calls) which affects the throughput for both TCP and UDP (especially for UDP).
    The latencies for TCP and UDP are quite close for Go and C.
    For both GO and C, the latency of TCP is slightly higher than UDP, but its throughput is much higher than UDP, since TCP can batch multiple messages and improve throughput.

## Slide 11: Fan-out
Setup
  Sender and receiver run on two different machines (Huawei S1 and S2).
  One message generation goroutine at sender side generates signal sending to each sending goroutine every 5ms which triggers the sending goroutine sending a 1000bytes message.
    Multiple connections between sender side and receiver side , each connection is handled by one goroutine at teach side.

## Slide 12: Fan-out (cont.)
Results
  For both protocols, the average latency increases as #of concurrent connections increases (due to more outliers with longer latency caused by concurrency).
  The average latency for TCP is slightly worse than UDP, the difference is not that significant. Socket difference is not the major bottleneck here.
  TCP has slightly higher user and system CPU utilization than UDP for most cases, since TCP socket is more complicated than UDP socket.
  However, when # of concurrent connections is 512, UDP has higher user and system CPU utilization, could be that the overhead of UDP in go net interface starts to play a role.
Chart: Protocol and Number of Concurrent Connections
| TCP 64 | UDP 64 | TCP 128 | UDP 128 | TCP 256 | UDP 256 | TCP 512 | UDP 512
usr cpu | 6.5 | 6.5 | 12 | 11.7 | 21.4 | 21.5 | 30 | 36.3
sys cpu | 21 | 19 | 40 | 34.4 | 70.3 | 65 | 106.4 | 113.8

## Slide 13: Fan-in
Setup
  Sender and receiver run on two different machines (Huawei S1 and S2).
  Multiple message generation goroutines at sender side, each generates signal sending to the sending goroutine every 5ms which triggers the sending goroutine sending a 1000bytes message.
    Only one connection between sender and receiver, which is handled by the sending goroutine at the sender side and receiving goroutine at the receiver side.

## Slide 14: Fan-in (cont.)
Results
  Latencies for both UDP and TCP are small, less than 0.1 ms.
  TCP has slightly higher latency than UDP which is consistent with one-to-one connection experiment.
  Latency for both protocols decreases as aggregated traffic increases (# of messages increases), could be that the impact of NAPI, where it’s more efficient with larger load of traffic.
  The CPU utilization are close for TCP and UDP. However, UDP has slightly higher user and system CPU utilization than TCP , since TCP can batch messages and therefore reduces # of sent packets.
Chart: Protocol and Number of Concurrent Connections
| TCP 64 | UDP 64 | TCP 128 | UDP 128 | TCP 256 | UDP 256 | TCP 512 | UDP 512
usr cpu | 14 | 14 | 25 | 25 | 40 | 43 | 62 | 65
sys cpu | 22 | 23 | 39 | 38 | 52 | 59 | 61 | 73.3
Notes: y axis start from 0.
explain the result more sightfully.

## Slide 15: Proposal
Conclusion from Experiment Results
  There’s no significant advantage of UDP over TCP in latency, especially when connection concurrency is high.
  For both TCP and UDP, they have significantly higher latency in high-concurrency scenario.
Proposed approach
  Build Reliable UDP Multicast solution (RM-UDP)
    Multicast reduces concurrency for Daemon, allowing Daemon to connect to multiple Subscribers with only one socket.
    Reliability is needed to recover from packet loss.
      Either at application or transport level
  Measure the performance of RM-UDP under different scenarios (e.g., for subscribers with high loss rate connection)
    If RM-UDP is inadequate for some cases, like subscribers have a high loss rate, we can explore another extension - Hybrid multicast-unicast option where
      Some Subscribers connect to RM-UDP Daemon.
      Some Subscribers connect to unicast TCP Daemon.

## Slide 16: Multicast For Distributed System
Requirements for multicast protocol
  Well supported by routers
  Suit for the RTM application
    Subscribers can join and leave the multicast group any time.
  Suit for distributed implementation of RTM
    Publishers of the same topic can be connected to multiple Daemons, each Daemons connects to the same set of Subscribers.
    Multiple nodes can send multicast within one multicast group.
PIM SM (Protocol Independent Multicast Sparse Mode)
  Widely supported by most routers and systems.
  Each node (either Daemon or Subscriber) can join and leave the multicast group.
  All the nodes can perform multicast within one multicast group, therefore all Daemons forwarding the same topic can multicast the messages within the same multicast group.

## Slide 17: Reliable UDP Multicast
Reliable UDP Multicast with PIM SM
  Enable end-to-end message reliable delivery.
  Dramatically reduces the complexity (socket numbers) in both Daemon and Subscriber side.
  Support for distributed implementation of RTM.
Setup for Daemon and Subscriber Connection:
  For each topic creates one multicast group using one multicast address in 224.0.0.0/4.
  Daemon: join a multicast group for each topic.
  Subscriber: join a multicast group for each topic.
Work scope:
  Change the message sending and receiving part of RTM Daemon and Subscriber.
  Add reliability mechanisms: sending window, ack or nack, retransmission & so on.

## Slide 18: Reference
[1] M. Mellia, M. Meo, and C. Casetti, “TCP smart framing: a segmentation algorithm to reduce TCP latency,” IEEE/ACM Transactions on Networking (TON), vol. 13, no. 2, pp. 316–329, 2005.
[2] A. Goel, C. Krasic, and J. Walpole, “Low-latency adaptive streaming over tcp,” ACM Transactions on Multimedia Computing, Communications, and Applications (TOMM), vol. 4, no. 3, pp. 20–20, Aug. 2008.
[3] Y. Gu and R. L. Grossman, “UDT: UDP-based data transfer for high-speed wide area networks,” Computer Networks, vol. 51, no. 7, pp. 1777–1799, May 2007.
[4] “Aeron - Efficient reliable UDP unicast, UDP multicast, and IPC message transport.” [Online]. Available: https://github.com/real-logic/Aeron. [Accessed: 15-Oct-2016].
[5] E. Jeong, S. Woo, M. Jamshed, H. Jeong, and S. Ihm, “mTCP: a highly scalable user-level TCP stack for multicore systems,” USENIX NSDI, 2014.
[6] S. Han, S. Marshall, and B. G. Chun, “MegaPipe: A New Programming Interface for Scalable Network I/O | USENIX,” USENIX OSDI, 2012.
[7] “Fastsocket.” [Online]. Available: https://github.com/fastos/fastsocket. [Accessed: 15-Oct-2016].