## Slide 1: RTM A New Real-Time Messaging Middleware
Washington University
Project Report
Sept. 26, 2016

## Slide 2: To-do List
QoS
  APIs for service class definition and SLA specification
  Rate control: prevent SLA violation
Advanced transport protocol
  Shared-memory, reliable UDP, multicast
  Run-time adaptation
Optimize CPU scheduling efficiency, scalability and persistency
Notes: From the last telecon

## Slide 3: QoS Model
Prioritization architecture
  Direct topics with different QoS requirements to different daemons
  Daemons are assigned with different scheduling priority
  Guarantee low-latency for latency-sensitive (with higher QoS requirement) topics
Rate Control
  Enforce SLA of any topic
  Prevent from the starvation of low-priority topics due to the SLA violation of high-priority topics

## Slide 4: QoS API
Lookup-daemon is used for directory service
During initiation, every RTM daemon has to register itself as high-priority/low-priority daemon at the lookup-daemon
During initiation, every producer has to specify its own priority, and visit lookup-daemon for the address of the RTM daemon with corresponding priority
  Then create a TCP connection between producer and a corresponding RTM daemon
  A high-priority producer can only publish msgs of high-priority topics
During initiation, every consumer queries the lookup-daemon for the address of the RTM daemon that handles the topic of interest. Then create a connection to that daemon

## Slide 5: Rate Control
Producer
User Code
Publisher 1
Topic 1
RTM Daemon
Channel 1-A
Channel 2-A
Channel 1-B
Producer
User Code
Publisher 2
Congestion
Signal
Topic 2
Client 1
Client 2
De-Congestion
Signal
IOLoop
MessagePump
MessagePump
MessagePump
MessagePump
IOLoop
Congestion
Signal
De-Congestion
Signal
Enforce topic-level rate limit
  Token bucket for each Topic
Fair sharing among producers of a common topic
Congestion/De-Congestion signal mechanism to backpressure congestion (to producers)
  Per-topic signal to mitigate HOL (Head of Line) blocking in producer

## Slide 6: Rate Control in Daemon

## Slide 7: Rate Control in Producer

## Slide 8: Advanced Design
Decide batch size for the Topic in congestion mode
  Batch size <= Topic.Bucket.Cap
  Small batch size reduces worst-case latency
    May increase CPU overhead
Ensure
  (client.queue.cap-high_watermark) > tcp buffer size
    Tcp buffer size: 4kB~ 16*4kB
  (high_watermark – low_watermark) > tcp buffer size
  Low_watermark > Topic.batch_size
Dynamically-allocated multi-queue structure
  Improve memory efficiency

## Slide 9: Rate Control
Cap(client.queue)=10k, high-watermark=0.6*cap, low-water-mark=0.3*cap
Producer1/2/3 all publish Topic1
  Assume the SLA of Topic1 bounds the throughput at 4k msgs/s
Producer1/2/3: send 1 msg in every 1 ms
  Producer1: there is a burst sending
    Last for 20 seconds
    During this duration, producer1 sends 3 msgs in every 1ms
In NSQ (bottom left): during “burst duration”, total throughput is 5k msgs, violating the rate limit of Topic1
In RTM (bottom right, token bucket setup of topic1 is (rate=4000, burst=100)): rate limiting is guaranteed throughout the timeline
  After the 20s burst-sending, there are large amount of msgs pending in the IOLoop (corresponding to producer1). In order to drain the pending msgs, Topic1 keeps working at its best rate (4k msgs/s). That’s why the “burst duration” in RTM is longer than 20s
  Congestion and De-congestion occur 8 times during “burst sending”

## Slide 10: Insights of Rate Control
Enforce the SLA of any topic
  Prevent from high CPU/bandwidth consumption caused by SLA violation
    Mitigate the starvation of low-priority daemon due to the misbehave of high-priority daemon
Mitigate intra-topic interference
  In NSQ, one misbehave producer is likely to starve other producers of the same topic
    Reason: producers of a common topic share a msg queue inside daemon. If the queue is over-used by one producer, msgs from other producers have to be either stored into disk or dropped immediately
  In RTM, our rate control provides fair sharing among producers of a common topic, protecting any producer from the intra-topic interference

## Slide 11: Latency Evaluation
Publisher 0:
  Publish topic 0
  sends 1 msg per 2 ms
  Collect 10k latency results
Publisher 1
  Publish topic 1
    Rate limit is 25k msgs/s
  Create 3 producers; each producer sends 25 msgs per 1 ms
    Total sending rate is 75k msgs/s
Publisher 2
  Publish topic 2; other setup same as Publisher 1
Publisher 3
  Publish topic 3; other setup same as Publisher 1

## Slide 12: Latency Evaluation
In NSQ
  Throughput (at receiver host) = 530 Mb/s (out of 1 Gb/s)
  CPU (at sender host) = 98.3% (out of 100%)
In RTM, the token bucket for every topic is: (25k, 500)
  Throughput (at receiver host) = 316 Mb/s
  CPU (at sender host) = 49.2%